EDEWG Change Request #097

This EDEWG Change Request can be found on the PUC website at http://www.puc.state.pa.us/electric/electric_edewg_download.aspx

| Requester’s Name: Joe Bisti | EDC Name: PECO Energy | Phone # : 215-841-5626 |
| --- | --- | --- |
| Date of Request: 2/2/2012 | Affected EDI Transaction Set #(s): 814E, 814C, 814R (electric only) | E-Mail Address: joseph.bisti@peco-energy.com |
| Requested Priority (emergency/high/low): High | Requested Implementation Date: 1Q of 2013 (tentative) | Status: Approved / pending redline to IGs |

Brief Explanation (This will be copied into the description in the Change Control Summary Spreadsheet):

THE FOLLOWING CHANGES ARE PROPOSED AS PECO-SPECIFIC WHILE OPTIONAL FOR OTHER PA EDCS.

The Implementation Guides for EDI 814 transactions currently indicate that PECO supports maintenance of ESP preferences for either summarized or detailed interval data at the ESP level.  In the first quarter of 2013 (tentatively), PECO intends to modify this relationship by converting this ESP-level preference to an account-level preference.

Additionally, within detailed interval data transactions (aka 867 Interval Usage transactions for billing), PECO plans to provide the capability for ESPs to request interval data at the meter level.  ESPs may also continue to receive detailed interval data at the summarized account level, as is the case today.  This is a new capability that the current Implementation Guides do not address which PECO also intends to introduce in early 2013 (tentatively).

This change control proposes specific modifications to the EDI 814 enrollment, change, and reinstatement Implementation Guides to support the above modifications.  Appendices to this form are included specifying proposed IG changes as well as various use cases to illustrate the flow of different scenarios.

Detail Explanation  (Exactly what change is required? To which EDEWG Standards? Why?):

1.  PECO to manage Interval Summary at acct-level:  PECO requests that all EDI 814 Implementation Guides be updated as applicable to indicate that PECO will maintain “Summary Interval” preferences at the account level rather than the ESP level.  PECO will adhere to the existing EDEWG standards relative to the LIN05 “SI” service to support this change.  An enrollment request not specifying a supplier’s preference for interval data via the REF*17 will be treated by default as a request for summary data, meaning that the ESP will receive an 867 MU at the time of billing.

NOTE:  PECO will set effective dates for EDI 814Cs sent by the ESP identically to the manner in which PECO sets effective dates for bill option changes; The change will be effective as of the next meter read date, meaning that the 867 subsequently sent to the ESP by PECO in association with that meter read date will be sent in the format specified by the ESP.

2.  PECO provides summary or detail but not both:  Some language in the IG indicates that the ESP can receive information at both the summary and the detail level.  PECO does not currently provide the information in both formats to the ESP for billing, nor does PECO have plans to do so.  ESPs may receive summarized OR detailed interval usage data for billing via the EDI 867, but not both.  Therefore, PECO requests that language implying that both can be sent be modified to indicate that, at a minimum, PECO cannot send both but rather will send one or the other.  The updates should also incorporate PECO’s proposed capability to provide detailed interval data at either the account or meter level (see Item 5 below).

3.  ADD new REF*MT*03 to 814E Resp, 814C Meter Exch (REF*NM1 = MX), & 814R for Interval Data Capability – PECO wishes to provide a means of informing suppliers that PECO is collecting interval data for a meter associated with an account.  As such, PECO proposes to add an additional segment to the REF*MT.  This segment would be the “REF03”, listed as a “Description” element and specifying “I” for availability of interval data or “M” for availability of only monthly data.  ESPs may reference this as an aid in determining the level of data required.

4.  Add “NIA” status code to REF*7G in EDI 814 Enrollment and Change IGs – If the ESP requests interval data for a non-interval account via the REF*17, PECO proposes to provide a rejection reason (REF*7G) in the response containing the reason code of “NIA”, “Not Interval Account”.  (NOTE:  For the 814E, this rejection code will be specific to the “SI” service.)

- Add new REF*17 code for meter-level interval detail within EDI 814E, 814C, and 814R – An ESP requesting detailed interval data on an account via the REF*17 requires the ability to specify whether they desire the associated EDI 867 Interval Usage transaction at the account level (currently provided by PECO) or at the meter level (forthcoming capability that PECO will offer).  Therefore, PECO proposes that an additional value be added to the current REF*17 standard for this purpose.  ESPs desiring account-level detail would submit REF*17*DETAIL, which will provide an 867IU transaction identical to what ESPs receive from PECO today for interval metered accounts.  ESPs desiring meter-level detail would submit REF*17*METERDETAIL, which will provide a meter-level 867IU transaction that PECO does not currently provide to ESPs.  (The REF*17*SUMMARY specification would remain as-is.)  Per existing EDEWG standards, PECO will echo back the REF*17 segment in the enrollment response as well as provide it in all 814R requests but not in the change response.

NOTES:  PECO will not initiate a change to the ESP related to this segment.

PECO provides the following in the appendix attached to this change control:

- Recommended EDEWG IG Updates

- Process flows and X12 examples (including request and response) for the following scenarios:

E1)  ESP enrollment, no data preference specified (implied summary preference)

E2)  ESP enrollment, requesting summary preference

E3)  ESP enrollment, requesting detailed interval data but not specifying account vs. meter level (implied as account-level preference)

E4)  ESP enrollment, requesting detailed interval data at the meter level, plus a secondary HU request

E5)  For non-interval account:  ESP enrollment, requesting detailed interval data

E6)  ESP change, from summary to detailed, specifying meter-level

E7)  ESP change, from detailed meter-level to summary

E8)  For non-interval account:  ESP change, from summary to detailed, specifying account-level

E9)  EDC meter exchange, with new meter providing interval data

E10)  EDC reinstatement, detailed account-level interval data

For Change Control Manager Use Only:

| Date of EDEWG Discussion: 2/2/2012, 3/1/2012 | Expected Implementation Date: 1Q 2013 (tentative) |  |
| --- | --- | --- |

EDEWG Discussion and Resolution:

2/2/12-Brandon Siegel:  Rcvd request, entered into tracking, assigned #097, and placed on 2/2 meeting agenda.

2/2/12 – Brandon Siegel:  EDEWG discussed.   PECO was asked to consider using the same REF7G code as PEPCO MD and the REF1P code in Ohio.   Brandon Siegel will review & consult with PECO.   EDI CC 97 remains open pending EDEWG approval.

2/8/12-Brandon Siegel:  Reviewed and consulted with PECO.   Modified EDI CC 97 to use NIA (Not Interval Account) in the REF7G of the 814E and 814C for PECO.   PECO agreed and the revised EDI CC was sent to the list server.

3/1/12-Brandon Siegel:   EDEWG discussed and approved EDI CC 97_Update.   Will be incorporated into next redline revision of IGs.

Priority Classifications

| Emergency Priority | Implemented within 10 days or otherwise directed by EDEWG |
| --- | --- |
| High Priority | Changes / Enhancements implemented with 30 days. The next release, or as otherwise directed by EDEWG |
| Low Priority | Changes / Enhancements implemented no earlier than 90 days, Future Release, or as otherwise directed by EDEWG |

Please submit this form via e-mail to both the PUC at annmarino@state.pa.us and to the

Change Control Manager, Brandon Siegel at bsiegel@ista-na.com

Index of Appendices

- 814 Enrollment IG – Proposed Changes

  - Proposed IG Changes

    - Pennsylvania Notes

    - Data Dictionary Updates

    - Updated Detailed Specification, REF*7G (add “UMA” code)

    - Updated Detailed Specification, New REF*MT*REF03 (Interval Data Capability)

    - Updated Detailed Specification, REF*17 (Additional REF02 Code for Interval Detail Level)

  - Process Flow

  - Sample X12

    - ESP enrollment, no data preference specified (implied as summary preference)

    - ESP enrollment, requesting summary preference

    - ESP enrollment, requesting detailed interval data but not specifying account vs. meter level (implied as account-level preference)

    - ESP enrollment, requesting detailed interval data at the meter level, plus a secondary HU request

    - For non-interval account:  ESP enrollment, requesting detailed interval data

- 814 Change IG – Proposed Changes

  - Proposed IG Changes

    - Pennsylvania Notes

    - Data Dictionary Updates

    - Updated Detailed Specification, REF*7G (add “UMA” code)

    - Updated Detailed Specification, REF*17 (Additional REF02 Code for Interval Detail Level)

    - Updated Detailed Specification, New REF*MT*REF03 (Interval Data Capability)

  - Process Flow

  - Sample X12

    - ESP change, from summary to detailed, specifying meter-level

    - ESP change, from detailed meter-level to summary

    - For non-interval account:  ESP change, from summary to detailed, specifying account-level

    - EDC meter exchange, with new meter providing interval data

- 814 Reinstatement IG – Proposed Changes

  - Proposed IG Changes

    - Data Dictionary Updates

    - Updated Detailed Specification, REF*17 (Additional REF02 Code for Interval Detail Level)

    - Updated Detailed Specification, New REF*MT*REF03 (Interval Data Capability)

  - Sample X12

- PECO EDC reinstatement, detailed account-level data

Updated Pennsylvania Notes reflecting new PECO default as summary and specifying that PECO does not provide both summary and detailed data for billing purposes

|  |  | Pennsylvania Notes |
| --- | --- | --- |
| Unknown LIN05 codes |  | PA Rules: If an LDC receives a request for a service that the state does not support, the LDC should reject it with a REF*7G*SDE*SERVICE DOES NOT EXIST If an LDC receives a request for a service that the state supports, but the LDC does not, the LDC should accept it, but then send a status code REF*1P*SNP*SERVICE NOT PROVIDED |
| Requesting Summary Only information for Interval Data (PA Only) |  | Every utility must provide the ability for a supplier to receive interval data at either the summary level or the detail level. The default, except for PPL EU and PECO, is that an ESP will receive interval data at the summary and the detail level. If an ESP wants interval data at both the summary and the detail level the ESP does not need to take any action. For PPL EU, because nearly all customers have interval meters, the default is for the ESP to receive summary data only. If an ESP wants interval data at both the summary and detail levels, the ESP must submit “SI” and include the REF*17*DETAIL segment. For PECO, the default is also for the ESP to receive summary data. If an ESP wants interval data at the detail level, the ESP must submit “SI” and specify account-level versus meter-level detail via the REF*17 segment. Please note that, unlike PPL EU, PECO does not provide interval data for billing at both the summary and detail levels; The ESP may receive either summary or detail, but not both. If an ESP wants to receive interval data at only the summary level, the ESP must: Contact the LDC to determine if the LDC supports summary level data by account or by ESP If the LDC supports summary level interval data by account, the ESP must submit “SI” in the LIN05 to indicate that only summary level interval data is requested for the account. If the LDC supports summary level interval data by ESP (PECO follows this practice), the “SI” in the LIN05 is not used. The ESP must call the supplier interface group at the LDC to request summary level interval data. The LDC will then return summary level interval data for ALL accounts for that ESP. For PPL EU, if an ESP wants interval data at both the summary and detail levels, the ESP must submit “SI” and include the REF*17*DETAIL segment As stated above, PECO does not provide interval data for billing at both the summary and detail levels; The ESP may receive either summary or detail, but not both. Responses to a Summary Interval Request (LIN05=SI): If the utility does not provide this capability by account, they will accept the request, but respond with a Status Reason code (1P) of SNP for “Service Not Provided”. Excluding PECO: If the utility provides this service by account, but the account is not an interval account, they will accept the request, but respond with a Status Reason code (1P) of UMA for “Unmetered or non-interval account”. PECO provides this service by account. If the account is not an interval account, PECO will reject the request, responding with a Status Reason code (7G) of NIA for “ Not interval account”. If the utility provides this service by account, and the account is an interval account, the utility will accept this request, and in their response send a REF*17*SUMMARY. |

Data Dictionary changes

Updated REF*17 with addition of PECO-specific codes

| Interval Reporting Level | Indicates that interval data will be reported at the level requested. | REF02= SUMMARY or DETAIL Or for PECO-only METERDETAIL (DETAIL = Account-Level Detail) | LIN: REF01= 17 | X(30) |
| --- | --- | --- | --- | --- |

Updated REF*MT (meter type) with addition of REF03 for interval data capability:

| 79 | Meter Type | Type of Meter | REF02 & REF03 | NM1: REF01= MT | X(5) |
| --- | --- | --- | --- | --- | --- |

Updated Detailed Specification, REF*7G (Rejection Reason – add “UMA” code)

# Segment:	REF Reference Identification (7G=Rejection Reason)

Position:	030

Loop:	LIN

Level:	Detail

Usage:	Optional

Max Use:	>1

Purpose:	To specify identifying information

Syntax Notes:	1	At least one of REF02 or REF03 is required.

- If either C04003 or C04004 is present, then the other is required.

- If either C04005 or C04006 is present, then the other is required.

Semantic Notes:	1	REF04 contains data relating to the value cited in REF02.

Comments:

| Notes: |  | This iteration of the REF segment is used to convey the rejection reason codes in response to a Request. The rejection reason codes are conveyed in this segment rather than in the ASI03 to allow for multiple rejection reasons. |
| --- | --- | --- |
| PA Use: |  | If an LDC receives a request for a service that the state does not support, the LDC should reject it with a REF*7G*SDE*SERVICE DOES NOT EXIST If an LDC receives a request for a service that the state supports, but the LDC does not, the LDC should accept it, but then send a status code REF*1P*SNP*SERVICE NOT PROVIDED |
|  |  | Request: Accept Response: Reject Response: | Not Used Not Used Required |
| NJ Use: |  | If an LDC receives a request for a service that it does not support (whether the state supports it or not), the LDC should accept it, but then send a status code REF*1P*SNP*SERVICE NOT PROVIDED |
| DE Use: |  | Same as NJ |
| MD Use: |  | Same as NJ |
| Example: |  | REF*7G*A13*ADDITIONAL REASON TEXT HERE |

Data Element Summary

Ref.	Data

Des.	Element	Name	X12 Attributes

| Must Use | REF01 | 128 | Reference Identification Qualifier | M | ID 2/3 |
| --- | --- | --- | --- | --- | --- |
|  | Code qualifying the Reference Identification |
|  | 7G |  | Data Quality Reject Reason |
|  | Reject reasons associated with a reject status notification. |

Rules for Rejection Reason Codes

The codes on the next several pages have been identified by the UIG to convey rejection reasons. Only the codes listed for each service are valid for that service. If you require additional codes, send an email to the appropriate state’s listserver. “A13” (Other) must only be used when an existing error code does not convey the reason correctly. Each time “A13” (Other) is used for a new purpose, an E-mail must be sent to the appropriate state’s listserver by the party sending the code, to notify the market participants about the text explanation for A13. This information will be compiled and new codes will be issued on a periodic basis. PA Listserver: edewg@ls.eei.org NJ Listserver: njbpu@ls.eei.org

| Summary Interval (SI) Rejection Codes: |
| --- |
| Must Use | REF02 | 127 | Reference Identification | X | AN 1/30 |
|  | Reference information as defined for a particular Transaction Set or as specified by the Reference Identification Qualifier |
|  | NIA |  | Not interval account |
| Optional | REF03 | 352 | Description | X | AN 1/80 |
|  | A free-form description to clarify the related data elements and their content |
|  | Used to further describe the status reason code sent in REF02. Codes “A13” and “API” require text explanation in this element. |

Updated Detailed Specification, REF*17 (Additional REF02 Codes for Interval Detail Level)

# Segment:	REF Reference Identification (17=Summary Interval)

Position:	030

Loop:	LIN

Level:	Detail

Usage:	Optional

Max Use:	>1

Purpose:	To specify identifying information

Syntax Notes:	1	At least one of REF02 or REF03 is required.

2	If either C04003 or C04004 is present, then the other is required.

3	If either C04005 or C04006 is present, then the other is required.

Semantic Notes:	1	REF04 contains data relating to the value cited in REF02.

Comments:

| PA Use: |  | Every utility must provide the ability for a supplier to receive interval data at either the summary level or the detail level. The default, except for PPL EU and PECO, is that an ESP will receive interval data at the summary and the detail level. If an ESP wants interval data at both the summary and the detail level the ESP does not need to take any action. For PPL EU, because nearly all customers have interval meters, the default is for the ESP to receive summary data only. If an ESP wants interval data at both the summary and detail levels, the ESP must submit “SI” and include the REF*17*DETAIL segment. For PECO, the default is also for the ESP to receive summary data only. If an ESP wants interval data at the detail level, the ESP must submit “SI” and specify account-level versus meter-level detail via the REF*17 segment. Please note that, unlike PPL EU, PECO does not provide interval data for billing at both the summary and detail levels; The ESP may receive either summary or detail, but not both If an ESP wants to receive interval data at only the summary level, the ESP must: Contact the LDC to determine if the LDC supports summary level data by account or by ESP If the LDC supports summary level interval data by account, the ESP must submit "SI" in the LIN05 to indicate that only summary level interval data is requested for the account. If the LDC supports summary level interval data by ESP, the "SI" in the LIN05 is not used. The ESP must call the supplier interface group at the LDC to request summary level interval data. The LDC will then return summary level interval data for ALL accounts for that ESP. For PPL EU, the default is summary. If an ESP wants interval data at both the summary and detail levels, the ESP must submit “SI” and include the REF*17*DETAIL segment. As stated above, PECO does not provide interval data for billing at both the summary and detail levels; The ESP may receive either summary or detail, but not both. Responses to a Summary Interval Request (LIN05=SI): If the utility does not provide this capability at the account level, they will accept the request, but respond with a Status Reason code (1P) of SNP for “Service Not Provided”. If the utility provides this service at the account level, but the account is not an interval account, they will accept the request, but respond with a Status Reason code (1P) of UMA for “Unmetered or non-interval account”. If the utility provides this service at the account level, and the account is an interval account, the utility will accept this request, and in their response send a REF*17*SUMMARY. |
| --- | --- | --- |
|  |  | SI Request: SI Accept Response: SI Reject Response All other Requests: All other Accept Responses: All other Reject Responses: | Required by PPL EU and PECO in the LIN loop where LIN05=SI if the ESP wants to receive Interval Details. Required if service was requested and will be provided. Not Used Not Used Not Used Not Used |
| NJ Use: |  | Optional for JCP&L and Atlantic City Electric |
| DE Use: |  | Not Used |
| MD Use: |  | Same as PA as far as 814 Enrollment transaction. Refer to General Notes section for each utility’s plans to provide interval details. |
| Example: |  | REF*17*SUMMARY |

Data Element Summary

Ref.	Data

Des.	Element	Name	X12 Attributes

| Must Use | REF01 | 128 | Reference Identification Qualifier | M | ID 2/3 |
| --- | --- | --- | --- | --- | --- |
|  | Code qualifying the Reference Identification |
|  | 17 |  | Client Reporting Category |
|  | Used to convey whether the ESP will receive summary only information, or detail and associated summary information for this interval account. |
| Must Use | REF02 | 127 | Reference Identification | X | AN 1/30 |
|  | Reference information as defined for a particular Transaction Set or as specified by the Reference Identification Qualifier |
|  | When REF01 is 17, valid values for REF02 are: SUMMARY – Metering party will send only summary level data for this interval account. DETAIL – Metering party will send interval details for this account. PECO will interpret this as account-level detail. PECO-Only: METERDETAIL – Metering party will send interval details for each meter on the account |

# Updated Detailed Specification, Add REF*MT*REF03 (Interval Data Capability)

## Segment:	REF Reference Identification (MT=Meter Type)

Position:	130

Loop:	NM1

Level:	Detail

Usage:	Optional

Max Use:	>1

Purpose:	To specify identifying information

Syntax Notes:	1	At least one of REF02 or REF03 is required.

2	If either C04003 or C04004 is present, then the other is required.

3	If either C04005 or C04006 is present, then the other is required.

Semantic Notes:	1	REF04 contains data relating to the value cited in REF02.

Comments:

| PA Use: |  | There will only be one REF*MT segment for each NM1 loop. If there are multiple meter types on this meter, only one REF*MT will be sent. It will contain the code COMBO. The specific meter type will be identified in the REF03 field in subsequent REF segments for this meter (i.e. REF*4P, REF*IX, REF*TU). |
| --- | --- | --- |
|  |  | Request: CE Accept Response: All other Accept Responses: Reject Response: | Not Used Required for each meter that is used for billing purposes. This segment will not be provided in the NM1 loop for UNMETERED services. Not Used Not Used |
| NJ Use: |  | Same as PA |
| DE Use: |  | Same as PA |
| MD Use: |  | Same as PA |
| Example: |  | REF*MT*KHMON or REF*MT*COMBO |

Data Element Summary

Ref.	Data

Des.	Element	Name	X12 Attributes

| Must Use | REF01 | 128 | Reference Identification Qualifier | M | ID 2/3 |
| --- | --- | --- | --- | --- | --- |
|  | Code qualifying the Reference Identification |
|  | MT |  | Meter Ticket Number |
|  | Meter Type |
| Must Use | REF02 | 127 | Reference Identification | X | AN 1/30 |
|  | Reference information as defined for a particular Transaction Set or as specified by the Reference Identification Qualifier |
|  | When REF01 is MT, the meter type is expressed as a five-character field. The first two characters are the type of consumption, the last three characters are the metering interval. “COMBO” is used for a meter that records more than one measurement. Valid values can be a combination of the following values: |
|  | Type of Consumption |  | Metering Interval |
|  | K1 | Kilowatt Demand |  | Nnn | Number of minutes from 001 to 999 |
|  | K2 | Kilovolt Amperes Reactive Demand |  | ANN | Annual |
|  | K3 | Kilovolt Amperes Reactive Hour |  | BIA | Bi-annual |
|  | K4 | Kilovolt Amperes |  | BIM | Bi-monthly |
|  | K5 | Kilovolt Amperes Reactive |  | DAY | Daily |
|  | KH | Kilowatt Hour |  | MON | Monthly |
|  | T9 | Thousand Kilowatt Hours |  | QTR | Quarterly |
|  | For Example: |
|  |  | KHMON | Kilowatt Hours Per Month |  |  |
|  |  | K1015 | Kilowatt Demand per 15 minute interval |  |  |
|  | Other Valid Codes |  |  |
|  | COMBO | This code is used to indicate that the meter has multiple measurements, e.g., one meter that measures both kWh and Demand. |

| Optional | REF03 | 127 | Reference Identification Qualifier | X | AN 1/80 |
| --- | --- | --- | --- | --- | --- |
|  | Reference information as defined for a particular Transaction Set or as specified by the Reference Identification Qualifier |
|  | NOTE: PECO (PA) is the only EDC currently populating this segment. When REF01 is MT, valid values for REF03 are: I – Interval data available M –Interval data not available |

Scenario 1:  ESP enrollment, no data preference specified (implied summary preference)

Bill-Ready EDI 814 enrollment

| BGN*13*199904011956531*19990401 | Request, unique transaction identification number, transaction creation date |
| --- | --- |
| N1*8S*LDC COMPANY*1*007909411**40 | LDC Name, LDC DUNS information, receiver |
| N1*SJ*ESP COMPANY*9*007909422ESP1**41 | ESP Name, ESP DUNS information, submitter |
| N1*8R*CUSTOMER NAME | Customer Name |
| LIN*CE1999123100002*SH*EL*SH*CE | Unique transaction reference number, enrollment request for electric generation services |
| ASI*7*021 | Request for addition |
| REF*11*2348400586 | ESP Account Number |
| REF*12*293839200 | LDC Account Number |
| REF*BLT*LDC | LDC consolidates the LDC and ESP charges |
| REF*PC*DUAL | Each party calculates its own charges (Bill Ready) |
| DTM*129*19990401*1430*ET | Date/time/time zone customer agreed to obtain service from the Service Provider |
| AMT*7N*1 | Participating interest: |

Bill-Ready EDI 814 enrollment response

| BGN*11*199904020830531*19990402***199904011956531 | Response, unique transaction identification number, transaction creation date and original request transaction identification number |
| --- | --- |
| N1*8S*LDC COMPANY*1*007909411**41 | LDC Name, LDC DUNS information, submitter |
| N1*SJ*ESP COMPANY*9*007909422ESP1**40 | ESP Name, ESP DUNS information, receiver |
| N1*8R*CUSTOMER NAME*92*1210 | Customer Name and reference number |
| N3*123 N MAIN ST*FLR 13 | Service address |
| N4*ANYTOWN*PA*18111 | City/State/Zip for Service Address. |
| PER*IC*MARY JONES*TE*8005559876 | Customer Contact name and telephone number |
| N1*BT*ACCOUNTS PAYABLE DEPT | Bill to party |
| N3*100 WEST AVENUE | Bill to address |
| N4*ANYTOWN*PA*18111 | Bill to City/State/Zip |
| PER*IC*KELLY WEST*TE*8005559876 | Bill To Contact name and telephone number |
| N1*PK*FRANK SMITH | Party to Receive Copy Name |
| N3*459 AVENUE B | Party to Receive Copy Address |
| N4*ANYTOWN*PA*18111 | Party to Receive Copy City/State/Zip |
| PER*IC*FRANK SMITH*TE*8005559876 | Party to Receive Copy Name |
| N1*2C*CAROL WRIGHT | Co-Participant Name |
| N3*23948 MAIN STREET | Co-Participant Address |
| N4*ANYTOWN*PA*18111 | Co-Participant City/State/Zip |
| PER*IC*CAROL WRIGHT*TE*8005559876 | Co-Participant Name and telephone number |
| LIN*CE1999123100002*SH*EL*SH*CE | Unique transaction reference number, enrollment request for electric generation services |
| ASI*WQ*021 | Accept Enrollment request |
| REF*11*2348400586 | ESP Account Number |
| REF*12*293839200 | LDC Account Number |
| REF*4N*N | LDC Payment Arrangement Status |
| REF*BF*18 | LDC Billing Cycle |
| REF*BLT*LDC | LDC consolidates the LDC and ESP charges |
| REF*PC*DUAL | Each party calculates its own charges (Bill Ready) |
| REF*NR*N | Budget Billing Status |
| REF*SPL**PJM192478939901287748 | Indicates PJM LMP Bus Number |
| DTM*129*19990401*1430*ET | Date/time/time zone customer agreed to obtain service from the Service Provider |
| DTM*150*19990425 | Estimated Start date |
| AMT*7N*1 | Participating interest |
| AMT*QY*1 | Eligible Load Percentage |
| AMT*5J*2 | Air conditioners in load cycling program |
| AMT*L0*1 | Water Heaters in load cycling program |
| AMT*KC*12.8 | Peak Load Capacity |
| AMT*KZ*14.1 | Network Service Peak Load |
| AMT*LD*12 | Number of months over which the total kWh and/or Peak Demand are calculated |
| AMT*MA*50 | Peak Demand |
| AMT*TA*125500 | Total kWh |
| NM1*MQ*3******32*123857G | Meter number |
| REF*LO*GS | LDC Load Profile |
| REF*NH*GS1 | LDC Rate class |
| REF*PR*123 | LDC Rate Subclass |
| REF*TZ*18 | LDC Meter Cycle |
| REF*MT*COMBO*I | Meter Type |
| REF*4P*1*KHMON | Meter constant on the kWh register |
| REF*IX*6.1*KHMON | Number of dials/digits |
| REF*TU*41*KHMON | Off Peak metering information sent on the 867 |
| REF*TU*42*KHMON | On Peak metering information sent on the 867 |
| REF*4P*1*K1MON | Meter constant on the demand (kW) register |
| REF*IX*5.0*K1MON | Number of dials/digits |
| REF*TU*41*K1MON | Off Peak metering information sent on the 867 |
| REF*TU*42*K1MON | On Peak metering information sent on the 867 |
| NM1*MQ*3******32*218737S | Meter Number |
| REF*LO*GS | LDC Load Profile |
| REF*NH*GS1 | LDC Rate class |
| REF*PR*123 | LDC Rate Subclass |
| REF*TZ*18 | LDC Meter Cycle |
| REF*MT*KHMON | Meter Type |
| REF*4P*1*KHMON | Meter Constant |
| REF*IX*5.0*KHMON | Number of dials/digits |
| REF*TU*51*KHMON | Totalized metering information sent on the 867 |

Scenario 2:  ESP enrollment, requesting summary data

Bill-Ready EDI 814 enrollment from ESP

| BGN*13*199904011956531*19990401 | Request, unique transaction identification number, transaction creation date |
| --- | --- |
| N1*8S*LDC COMPANY*1*007909411**40 | LDC Name, LDC DUNS information, receiver |
| N1*SJ*ESP COMPANY*9*007909422ESP1**41 | ESP Name, ESP DUNS information, submitter |
| N1*8R*CUSTOMER NAME | Customer Name |
| LIN*CE1999123100002*SH*EL*SH*CE | Unique transaction reference number, enrollment request for electric generation services |
| ASI*7*021 | Request for addition |
| REF*11*2348400586 | ESP Account Number |
| REF*12*293839200 | LDC Account Number |
| REF*BLT*LDC | LDC consolidates the LDC and ESP charges |
| REF*PC*DUAL | Each party calculates its own charges (Bill Ready) |
| DTM*129*19990401*1430*ET | Date/time/time zone customer agreed to obtain service from the Service Provider |
| AMT*7N*1 | Participating interest: |
| LIN*SI1999040111956532*SH*EL*SH*SI | Unique transaction reference number, request for electric summary only interval data |
| ASI*7*021 | Request for addition |
| REF*11*2348400586 | ESP Account Number |
| REF*12*293839200 | LDC Account Number |
| REF*17*SUMMARY | Summary/Interval Indicator |

Bill-Ready EDI 814 enrollment response from EDC

| BGN*11*199904020830531*19990402***199904011956531 | Response, unique transaction identification number, transaction creation date and original request transaction identification number |
| --- | --- |
| N1*8S*LDC COMPANY*1*007909411**41 | LDC Name, LDC DUNS information, submitter |
| N1*SJ*ESP COMPANY*9*007909422ESP1**40 | ESP Name, ESP DUNS information, receiver |
| N1*8R*CUSTOMER NAME*92*1210 | Customer Name and reference number |
| N3*123 N MAIN ST*FLR 13 | Service address |
| N4*ANYTOWN*PA*18111 | City/State/Zip for Service Address. |
| PER*IC*MARY JONES*TE*8005559876 | Customer Contact name and telephone number |
| N1*BT*ACCOUNTS PAYABLE DEPT | Bill to party |
| N3*100 WEST AVENUE | Bill to address |
| N4*ANYTOWN*PA*18111 | Bill to City/State/Zip |
| PER*IC*KELLY WEST*TE*8005559876 | Bill To Contact name and telephone number |
| N1*PK*FRANK SMITH | Party to Receive Copy Name |
| N3*459 AVENUE B | Party to Receive Copy Address |
| N4*ANYTOWN*PA*18111 | Party to Receive Copy City/State/Zip |
| PER*IC*FRANK SMITH*TE*8005559876 | Party to Receive Copy Name |
| N1*2C*CAROL WRIGHT | Co-Participant Name |
| N3*23948 MAIN STREET | Co-Participant Address |
| N4*ANYTOWN*PA*18111 | Co-Participant City/State/Zip |
| PER*IC*CAROL WRIGHT*TE*8005559876 | Co-Participant Name and telephone number |
| LIN*CE1999123100002*SH*EL*SH*CE | Unique transaction reference number, enrollment request for electric generation services |
| ASI*WQ*021 | Accept Enrollment request |
| REF*11*2348400586 | ESP Account Number |
| REF*12*293839200 | LDC Account Number |
| REF*4N*N | LDC Payment Arrangement Status |
| REF*BF*18 | LDC Billing Cycle |
| REF*BLT*LDC | LDC consolidates the LDC and ESP charges |
| REF*PC*DUAL | Each party calculates its own charges (Bill Ready) |
| REF*NR*N | Budget Billing Status |
| REF*SPL**PJM192478939901287748 | Indicates PJM LMP Bus Number |
| DTM*129*19990401*1430*ET | Date/time/time zone customer agreed to obtain service from the Service Provider |
| DTM*150*19990425 | Estimated Start date |
| AMT*7N*1 | Participating interest |
| AMT*QY*1 | Eligible Load Percentage |
| AMT*5J*2 | Air conditioners in load cycling program |
| AMT*L0*1 | Water Heaters in load cycling program |
| AMT*KC*12.8 | Peak Load Capacity |
| AMT*KZ*14.1 | Network Service Peak Load |
| AMT*LD*12 | Number of months over which the total kWh and/or Peak Demand are calculated |
| AMT*MA*50 | Peak Demand |
| AMT*TA*125500 | Total kWh |
| NM1*MQ*3******32*123857G | Meter number |
| REF*LO*GS | LDC Load Profile |
| REF*NH*GS1 | LDC Rate class |
| REF*PR*123 | LDC Rate Subclass |
| REF*TZ*18 | LDC Meter Cycle |
| REF*MT*COMBO*I | Meter Type |
| REF*4P*1*KHMON | Meter constant on the kWh register |
| REF*IX*6.1*KHMON | Number of dials/digits |
| REF*TU*41*KHMON | Off Peak metering information sent on the 867 |
| REF*TU*42*KHMON | On Peak metering information sent on the 867 |
| REF*4P*1*K1MON | Meter constant on the demand (kW) register |
| REF*IX*5.0*K1MON | Number of dials/digits |
| REF*TU*41*K1MON | Off Peak metering information sent on the 867 |
| REF*TU*42*K1MON | On Peak metering information sent on the 867 |
| NM1*MQ*3******32*218737S | Meter Number |
| REF*LO*GS | LDC Load Profile |
| REF*NH*GS1 | LDC Rate class |
| REF*PR*123 | LDC Rate Subclass |
| REF*TZ*18 | LDC Meter Cycle |
| REF*MT*KHMON | Meter Type |
| REF*4P*1*KHMON | Meter Constant |
| REF*IX*5.0*KHMON | Number of dials/digits |
| REF*TU*51*KHMON | Totalized metering information sent on the 867 |
| LIN* SI1999040111956532*SH*EL*SH*SI | Unique transaction reference number, request for electric Meter Information |
| ASI*WQ*021 | Request for inquiry was Accepted |
| REF*11*2348400586 | ESP Account Number |
| REF*12*293839200 | LDC Account Number |
| REF*17*SUMMARY | Summary/Interval Indicator |

Scenario 3:  ESP enrollment, requesting detailed interval data (account-level preference)

Bill-Ready EDI 814 enrollment from ESP

| BGN*13*199904011956531*19990401 | Request, unique transaction identification number, transaction creation date |
| --- | --- |
| N1*8S*LDC COMPANY*1*007909411**40 | LDC Name, LDC DUNS information, receiver |
| N1*SJ*ESP COMPANY*9*007909422ESP1**41 | ESP Name, ESP DUNS information, submitter |
| N1*8R*CUSTOMER NAME | Customer Name |
| LIN*CE1999123100002*SH*EL*SH*CE | Unique transaction reference number, enrollment request for electric generation services |
| ASI*7*021 | Request for addition |
| REF*11*2348400586 | ESP Account Number |
| REF*12*293839200 | LDC Account Number |
| REF*BLT*LDC | LDC consolidates the LDC and ESP charges |
| REF*PC*DUAL | Each party calculates its own charges (Bill Ready) |
| DTM*129*19990401*1430*ET | Date/time/time zone customer agreed to obtain service from the Service Provider |
| AMT*7N*1 | Participating interest: |
| LIN*SI1999040111956532*SH*EL*SH*SI | Unique transaction reference number, request for electric summary only interval data |
| ASI*7*021 | Request for addition |
| REF*11*2348400586 | ESP Account Number |
| REF*12*293839200 | LDC Account Number |
| REF*17*DETAIL | Summary/Interval Indicator |

Bill-Ready EDI 814 enrollment response from EDC

| BGN*11*199904020830531*19990402***199904011956531 | Response, unique transaction identification number, transaction creation date and original request transaction identification number |
| --- | --- |
| N1*8S*LDC COMPANY*1*007909411**41 | LDC Name, LDC DUNS information, submitter |
| N1*SJ*ESP COMPANY*9*007909422ESP1**40 | ESP Name, ESP DUNS information, receiver |
| N1*8R*CUSTOMER NAME*92*1210 | Customer Name and reference number |
| N3*123 N MAIN ST*FLR 13 | Service address |
| N4*ANYTOWN*PA*18111 | City/State/Zip for Service Address. |
| PER*IC*MARY JONES*TE*8005559876 | Customer Contact name and telephone number |
| N1*BT*ACCOUNTS PAYABLE DEPT | Bill to party |
| N3*100 WEST AVENUE | Bill to address |
| N4*ANYTOWN*PA*18111 | Bill to City/State/Zip |
| PER*IC*KELLY WEST*TE*8005559876 | Bill To Contact name and telephone number |
| N1*PK*FRANK SMITH | Party to Receive Copy Name |
| N3*459 AVENUE B | Party to Receive Copy Address |
| N4*ANYTOWN*PA*18111 | Party to Receive Copy City/State/Zip |
| PER*IC*FRANK SMITH*TE*8005559876 | Party to Receive Copy Name |
| N1*2C*CAROL WRIGHT | Co-Participant Name |
| N3*23948 MAIN STREET | Co-Participant Address |
| N4*ANYTOWN*PA*18111 | Co-Participant City/State/Zip |
| PER*IC*CAROL WRIGHT*TE*8005559876 | Co-Participant Name and telephone number |
| LIN*CE1999123100002*SH*EL*SH*CE | Unique transaction reference number, enrollment request for electric generation services |
| ASI*WQ*021 | Accept Enrollment request |
| REF*11*2348400586 | ESP Account Number |
| REF*12*293839200 | LDC Account Number |
| REF*4N*N | LDC Payment Arrangement Status |
| REF*BF*18 | LDC Billing Cycle |
| REF*BLT*LDC | LDC consolidates the LDC and ESP charges |
| REF*PC*DUAL | Each party calculates its own charges (Bill Ready) |
| REF*NR*N | Budget Billing Status |
| REF*SPL**PJM192478939901287748 | Indicates PJM LMP Bus Number |
| DTM*129*19990401*1430*ET | Date/time/time zone customer agreed to obtain service from the Service Provider |
| DTM*150*19990425 | Estimated Start date |
| AMT*7N*1 | Participating interest |
| AMT*QY*1 | Eligible Load Percentage |
| AMT*5J*2 | Air conditioners in load cycling program |
| AMT*L0*1 | Water Heaters in load cycling program |
| AMT*KC*12.8 | Peak Load Capacity |
| AMT*KZ*14.1 | Network Service Peak Load |
| AMT*LD*12 | Number of months over which the total kWh and/or Peak Demand are calculated |
| AMT*MA*50 | Peak Demand |
| AMT*TA*125500 | Total kWh |
| NM1*MQ*3******32*123857G | Meter number |
| REF*LO*GS | LDC Load Profile |
| REF*NH*GS1 | LDC Rate class |
| REF*PR*123 | LDC Rate Subclass |
| REF*TZ*18 | LDC Meter Cycle |
| REF*MT*COMBO*I | Meter Type |
| REF*4P*1*KHMON | Meter constant on the kWh register |
| REF*IX*6.1*KHMON | Number of dials/digits |
| REF*TU*41*KHMON | Off Peak metering information sent on the 867 |
| REF*TU*42*KHMON | On Peak metering information sent on the 867 |
| REF*4P*1*K1MON | Meter constant on the demand (kW) register |
| REF*IX*5.0*K1MON | Number of dials/digits |
| REF*TU*41*K1MON | Off Peak metering information sent on the 867 |
| REF*TU*42*K1MON | On Peak metering information sent on the 867 |
| NM1*MQ*3******32*218737S | Meter Number |
| REF*LO*GS | LDC Load Profile |
| REF*NH*GS1 | LDC Rate class |
| REF*PR*123 | LDC Rate Subclass |
| REF*TZ*18 | LDC Meter Cycle |
| REF*MT*KHMON | Meter Type |
| REF*4P*1*KHMON | Meter Constant |
| REF*IX*5.0*KHMON | Number of dials/digits |
| REF*TU*51*KHMON | Totalized metering information sent on the 867 |
| LIN* SI1999040111956532*SH*EL*SH*SI | Unique transaction reference number, request for electric Meter Information |
| ASI*WQ*021 | Request for inquiry was Accepted |
| REF*11*2348400586 | ESP Account Number |
| REF*12*293839200 | LDC Account Number |
| REF*17*DETAIL | Summary/Interval Indicator |

Scenario 4:  ESP enrollment, requesting detailed interval data at the meter level, plus a secondary HU request

Bill-Ready EDI 814 enrollment from ESP

| BGN*13*199904011956531*19990401 | Request, unique transaction identification number, transaction creation date |
| --- | --- |
| N1*8S*LDC COMPANY*1*007909411**40 | LDC Name, LDC DUNS information, receiver |
| N1*SJ*ESP COMPANY*9*007909422ESP1**41 | ESP Name, ESP DUNS information, submitter |
| N1*8R*CUSTOMER NAME | Customer Name |
| LIN*CE1999123100002*SH*EL*SH*CE | Unique transaction reference number, enrollment request for electric generation services |
| ASI*7*021 | Request for addition |
| REF*11*2348400586 | ESP Account Number |
| REF*12*293839200 | LDC Account Number |
| REF*BLT*LDC | LDC consolidates the LDC and ESP charges |
| REF*PC*DUAL | Each party calculates its own charges (Bill Ready) |
| DTM*129*19990401*1430*ET | Date/time/time zone customer agreed to obtain service from the Service Provider |
| AMT*7N*1 | Participating interest: |
| LIN*SI1999040111956532*SH*EL*SH*SI | Unique transaction reference number, request for electric summary only interval data |
| ASI*7*021 | Request for addition |
| REF*11*2348400586 | ESP Account Number |
| REF*12*293839200 | LDC Account Number |
| REF*17*METERDETAIL | Summary/Interval Indicator |
| LIN* SI1999040111956533*SH*EL*SH*HU | Unique transaction reference number, request for electric Historical Usage |
| ASI*7*029 | Request for inquiry |
| REF*11*2348400586 | ESP Account Number |
| REF*12*293839200 | LDC Account Number |

Bill-Ready EDI 814 enrollment response from EDC

| BGN*11*199904020830531*19990402***199904011956531 | Response, unique transaction identification number, transaction creation date and original request transaction identification number |
| --- | --- |
| N1*8S*LDC COMPANY*1*007909411**41 | LDC Name, LDC DUNS information, submitter |
| N1*SJ*ESP COMPANY*9*007909422ESP1**40 | ESP Name, ESP DUNS information, receiver |
| N1*8R*CUSTOMER NAME*92*1210 | Customer Name and reference number |
| N3*123 N MAIN ST*FLR 13 | Service address |
| N4*ANYTOWN*PA*18111 | City/State/Zip for Service Address. |
| PER*IC*MARY JONES*TE*8005559876 | Customer Contact name and telephone number |
| N1*BT*ACCOUNTS PAYABLE DEPT | Bill to party |
| N3*100 WEST AVENUE | Bill to address |
| N4*ANYTOWN*PA*18111 | Bill to City/State/Zip |
| PER*IC*KELLY WEST*TE*8005559876 | Bill To Contact name and telephone number |
| N1*PK*FRANK SMITH | Party to Receive Copy Name |
| N3*459 AVENUE B | Party to Receive Copy Address |
| N4*ANYTOWN*PA*18111 | Party to Receive Copy City/State/Zip |
| PER*IC*FRANK SMITH*TE*8005559876 | Party to Receive Copy Name |
| N1*2C*CAROL WRIGHT | Co-Participant Name |
| N3*23948 MAIN STREET | Co-Participant Address |
| N4*ANYTOWN*PA*18111 | Co-Participant City/State/Zip |
| PER*IC*CAROL WRIGHT*TE*8005559876 | Co-Participant Name and telephone number |
| LIN*CE1999123100002*SH*EL*SH*CE | Unique transaction reference number, enrollment request for electric generation services |
| ASI*WQ*021 | Accept Enrollment request |
| REF*11*2348400586 | ESP Account Number |
| REF*12*293839200 | LDC Account Number |
| REF*4N*N | LDC Payment Arrangement Status |
| REF*BF*18 | LDC Billing Cycle |
| REF*BLT*LDC | LDC consolidates the LDC and ESP charges |
| REF*PC*DUAL | Each party calculates its own charges (Bill Ready) |
| REF*NR*N | Budget Billing Status |
| REF*SPL**PJM192478939901287748 | Indicates PJM LMP Bus Number |
| DTM*129*19990401*1430*ET | Date/time/time zone customer agreed to obtain service from the Service Provider |
| DTM*150*19990425 | Estimated Start date |
| AMT*7N*1 | Participating interest |
| AMT*QY*1 | Eligible Load Percentage |
| AMT*5J*2 | Air conditioners in load cycling program |
| AMT*L0*1 | Water Heaters in load cycling program |
| AMT*KC*12.8 | Peak Load Capacity |
| AMT*KZ*14.1 | Network Service Peak Load |
| AMT*LD*12 | Number of months over which the total kWh and/or Peak Demand are calculated |
| AMT*MA*50 | Peak Demand |
| AMT*TA*125500 | Total kWh |
| NM1*MQ*3******32*123857G | Meter number |
| REF*LO*GS | LDC Load Profile |
| REF*NH*GS1 | LDC Rate class |
| REF*PR*123 | LDC Rate Subclass |
| REF*TZ*18 | LDC Meter Cycle |
| REF*MT*COMBO*I | Meter Type |
| REF*4P*1*KHMON | Meter constant on the kWh register |
| REF*IX*6.1*KHMON | Number of dials/digits |
| REF*TU*41*KHMON | Off Peak metering information sent on the 867 |
| REF*TU*42*KHMON | On Peak metering information sent on the 867 |
| REF*4P*1*K1MON | Meter constant on the demand (kW) register |
| REF*IX*5.0*K1MON | Number of dials/digits |
| REF*TU*41*K1MON | Off Peak metering information sent on the 867 |
| REF*TU*42*K1MON | On Peak metering information sent on the 867 |
| NM1*MQ*3******32*218737S | Meter Number |
| REF*LO*GS | LDC Load Profile |
| REF*NH*GS1 | LDC Rate class |
| REF*PR*123 | LDC Rate Subclass |
| REF*TZ*18 | LDC Meter Cycle |
| REF*MT*KHMON | Meter Type |
| REF*4P*1*KHMON | Meter Constant |
| REF*IX*5.0*KHMON | Number of dials/digits |
| REF*TU*51*KHMON | Totalized metering information sent on the 867 |
| LIN* SI1999040111956532*SH*EL*SH*SI | Unique transaction reference number, request for electric Meter Information |
| ASI*WQ*021 | Request for inquiry was Accepted |
| REF*11*2348400586 | ESP Account Number |
| REF*12*293839200 | LDC Account Number |
| REF*17*METERDETAIL | Summary/Interval Indicator |

.

PECO would also send an EDI 814 HU response (acceptance) and EDI 867 HU (not shown).

Scenario 5:  For NON-INTERVAL account:  ESP enrollment, requesting detailed interval data

Bill-Ready EDI 814 enrollment from ESP

| BGN*13*199904011956531*19990401 | Request, unique transaction identification number, transaction creation date |
| --- | --- |
| N1*8S*LDC COMPANY*1*007909411**40 | LDC Name, LDC DUNS information, receiver |
| N1*SJ*ESP COMPANY*9*007909422ESP1**41 | ESP Name, ESP DUNS information, submitter |
| N1*8R*CUSTOMER NAME | Customer Name |
| LIN*CE1999123100002*SH*EL*SH*CE | Unique transaction reference number, enrollment request for electric generation services |
| ASI*7*021 | Request for addition |
| REF*11*2348400586 | ESP Account Number |
| REF*12*293839200 | LDC Account Number |
| REF*BLT*LDC | LDC consolidates the LDC and ESP charges |
| REF*PC*DUAL | Each party calculates its own charges (Bill Ready) |
| DTM*129*19990401*1430*ET | Date/time/time zone customer agreed to obtain service from the Service Provider |
| AMT*7N*1 | Participating interest: |
| LIN*SI1999040111956532*SH*EL*SH*SI | Unique transaction reference number, request for electric summary only interval data |
| ASI*7*021 | Request for addition |
| REF*11*2348400586 | ESP Account Number |
| REF*12*293839200 | LDC Account Number |
| REF*17*DETAIL | Summary/Interval Indicator |

Bill-Ready EDI 814 enrollment response from EDC

| BGN*11*199904020830531*19990402***199904011956531 | Response, unique transaction identification number, transaction creation date and original request transaction identification number |
| --- | --- |
| N1*8S*LDC COMPANY*1*007909411**41 | LDC Name, LDC DUNS information, submitter |
| N1*SJ*ESP COMPANY*9*007909422ESP1**40 | ESP Name, ESP DUNS information, receiver |
| N1*8R*CUSTOMER NAME*92*1210 | Customer Name and reference number |
| N3*123 N MAIN ST*FLR 13 | Service address |
| N4*ANYTOWN*PA*18111 | City/State/Zip for Service Address. |
| PER*IC*MARY JONES*TE*8005559876 | Customer Contact name and telephone number |
| N1*BT*ACCOUNTS PAYABLE DEPT | Bill to party |
| N3*100 WEST AVENUE | Bill to address |
| N4*ANYTOWN*PA*18111 | Bill to City/State/Zip |
| PER*IC*KELLY WEST*TE*8005559876 | Bill To Contact name and telephone number |
| N1*PK*FRANK SMITH | Party to Receive Copy Name |
| N3*459 AVENUE B | Party to Receive Copy Address |
| N4*ANYTOWN*PA*18111 | Party to Receive Copy City/State/Zip |
| PER*IC*FRANK SMITH*TE*8005559876 | Party to Receive Copy Name |
| N1*2C*CAROL WRIGHT | Co-Participant Name |
| N3*23948 MAIN STREET | Co-Participant Address |
| N4*ANYTOWN*PA*18111 | Co-Participant City/State/Zip |
| PER*IC*CAROL WRIGHT*TE*8005559876 | Co-Participant Name and telephone number |
| LIN*CE1999123100002*SH*EL*SH*CE | Unique transaction reference number, enrollment request for electric generation services |
| ASI*WQ*021 | Accept Enrollment request |
| REF*11*2348400586 | ESP Account Number |
| REF*12*293839200 | LDC Account Number |
| REF*4N*N | LDC Payment Arrangement Status |
| REF*BF*18 | LDC Billing Cycle |
| REF*BLT*LDC | LDC consolidates the LDC and ESP charges |
| REF*PC*DUAL | Each party calculates its own charges (Bill Ready) |
| REF*NR*N | Budget Billing Status |
| REF*SPL**PJM192478939901287748 | Indicates PJM LMP Bus Number |
| DTM*129*19990401*1430*ET | Date/time/time zone customer agreed to obtain service from the Service Provider |
| DTM*150*19990425 | Estimated Start date |
| AMT*7N*1 | Participating interest |
| AMT*QY*1 | Eligible Load Percentage |
| AMT*5J*2 | Air conditioners in load cycling program |
| AMT*L0*1 | Water Heaters in load cycling program |
| AMT*KC*12.8 | Peak Load Capacity |
| AMT*KZ*14.1 | Network Service Peak Load |
| AMT*LD*12 | Number of months over which the total kWh and/or Peak Demand are calculated |
| AMT*MA*50 | Peak Demand |
| AMT*TA*125500 | Total kWh |
| NM1*MQ*3******32*123857G | Meter number |
| REF*LO*GS | LDC Load Profile |
| REF*NH*GS1 | LDC Rate class |
| REF*PR*123 | LDC Rate Subclass |
| REF*TZ*18 | LDC Meter Cycle |
| REF*MT*COMBO*M | Meter Type |
| REF*4P*1*KHMON | Meter constant on the kWh register |
| REF*IX*6.1*KHMON | Number of dials/digits |
| REF*TU*41*KHMON | Off Peak metering information sent on the 867 |
| REF*TU*42*KHMON | On Peak metering information sent on the 867 |
| REF*4P*1*K1MON | Meter constant on the demand (kW) register |
| REF*IX*5.0*K1MON | Number of dials/digits |
| REF*TU*41*K1MON | Off Peak metering information sent on the 867 |
| REF*TU*42*K1MON | On Peak metering information sent on the 867 |
| NM1*MQ*3******32*218737S | Meter Number |
| REF*LO*GS | LDC Load Profile |
| REF*NH*GS1 | LDC Rate class |
| REF*PR*123 | LDC Rate Subclass |
| REF*TZ*18 | LDC Meter Cycle |
| REF*MT*KHMON | Meter Type |
| REF*4P*1*KHMON | Meter Constant |
| REF*IX*5.0*KHMON | Number of dials/digits |
| REF*TU*51*KHMON | Totalized metering information sent on the 867 |
| LIN* SI1999040111956532*SH*EL*SH*SI | Unique transaction reference number, request for electric Meter Information |
| ASI*U*021 | Request for inquiry was Rejected |
| REF*7G*NIA*NOT INTERVAL ACCOUNT | Status reason code |
| REF*11*2348400586 | ESP Account Number |
| REF*12*293839200 | LDC Account Number |

Updated Pennsylvania Notes specifying that PECO does not provide both summary and detailed data for billing purposes and that PECO provides services by account.

|  |  | Pennsylvania Notes |
| --- | --- | --- |
| Requesting Summary Only information for Interval Data (PECO Only) |  | PECO will not provide interval data for billing at both the summary and detail levels; The ESP may receive either summary or detail, but not both. PECO provides this service by account. If the account is not an interval account, PECO will reject the request, responding with a Status Reason code (7G) of UMA for “Unmetered or non-interval account”. |

Data Dictionary changes

Updated REF*17 with addition of PECO-specific codes

| Interval Reporting Level | Indicates that interval data will be reported at the level requested. | REF02= SUMMARY or DETAIL Or for PECO-only METERDETAIL (DETAIL = Account-Level Detail) | LIN: REF01= 17 | X(30) |
| --- | --- | --- | --- | --- |

Updated REF*MT (meter type) with addition of REF03 for interval data capability:

| 79 | Meter Type | Type of Meter | REF02 & REF03 | NM1: REF01= MT | X(5) |
| --- | --- | --- | --- | --- | --- |

Updated Detailed Specification, REF*7G (Rejection Reason – add “UMA” code)

# Segment:	REF Reference Identification (7G=Rejection Reason)

Position:	030

Loop:	LIN

Level:	Detail

Usage:	Optional

Max Use:	>1

Purpose:	To specify identifying information

Syntax Notes:	1	At least one of REF02 or REF03 is required.

2	If either C04003 or C04004 is present, then the other is required.

3	If either C04005 or C04006 is present, then the other is required.

Semantic Notes:	1	REF04 contains data relating to the value cited in REF02.

Comments:

| Notes: |  | This iteration of the REF segment is used to convey the rejection reason codes in response to a Request. The rejection reason codes are conveyed in this segment rather than in the ASI03 to allow for multiple rejection reasons. |
| --- | --- | --- |
| PA Use: |  | If an LDC receives a request for a service that the state does not support, the LDC should reject it with a REF*7G* SDE*SERVICE DOES NOT EXIST If an LDC receives a request for a service that the state supports, but the LDC does not, the LDC should accept it, but then send a status code REF*1P*SNP*SERVICE NOT PROVIDED |
|  |  | Request: Accept Response: Reject Response: | Not Used Not Used Required |
| NJ Use: |  | If an LDC receives a request for a service that it does not support (whether the state supports it or not), the LDC should accept it, but then send a status code REF*1P*SNP*SERVICE NOT PROVIDED |
| DE Use: |  | Same as NJ |
| MD Use: |  | Same as NJ |
| Example: |  | REF*7G*A13*ADDITIONAL REASON TEXT HERE |

Data Element Summary

Ref.	Data

Des.	Element	Name	X12 Attributes

| Must Use | REF01 | 128 | Reference Identification Qualifier | M | ID 2/3 |
| --- | --- | --- | --- | --- | --- |
|  | Code qualifying the Reference Identification |
|  | 7G |  | Data Quality Reject Reason |
|  | Reject reasons associated with a reject status notification. |

Rules for Rejection Reason Codes

| The codes on the next several pages have been identified by the UIG to convey rejection reasons. Only the codes listed for each service are valid for that service. If you require additional codes, send an email to the appropriate state’s listserver. “A13” (Other) must only be used when an existing error code does not convey the reason correctly. Each time “A13” (Other) is used for a new purpose, an E-mail must be sent to the appropriate state’s listserver by the party sending the code, to notify the market participants about the text explanation for A13. This information will be compiled and new codes will be issued on a periodic basis. PA Listserver: edewg@ls.eei.org NJ Listserver: njbpu@ls.eei.org |
| --- |
| Must Use | REF02 | 127 | Reference Identification | X | AN 1/30 |
|  | Reference information as defined for a particular Transaction Set or as specified by the Reference Identification Qualifier |
|  | 008 |  | Account exists but is not active |
|  | A13 |  | Other |
|  | REF03 Required. Send email to edewg@ls.eei.org each time A13 is used for a new purpose. |
|  | A76 |  | Account not found |
|  |  |  | This includes invalid account numbers as well as no account number being found. |
|  | A77 |  | Name specified does not match account |
|  | Allegheny Power Only – Allegheny will match on the first four characters of the last name or company name as it appears on the customer’s bill. |
|  | A84 |  | Invalid Relationship (not ESP of record) |
|  | A91 |  | Service is not offered at customer’s location |
|  | For instance, used to indicate that this is a gas only account, no electric service exists on the account. |
|  | ABN |  | Duplicate request received |
|  | ANL |  | Service provider not licensed to provide requested service |
|  | Also used if supplier sends billing address change, and is not the billing agent. |
|  | ANQ |  | Billing Agent not certified by utility |
|  | Not valid in NJ |
|  | API |  | Required information missing (REF03 Required) |
|  | C02 |  | Customer on Credit Hold |
|  | Valid in PA and NJ when consolidated bill requested for customer who has been switched to DUAL billing due to delinquencies when making the other party whole. |
|  | C11 |  | Change reason (REF*TD) missing or invalid |
|  | C13 |  | Multiple Change Request Not Supported |
|  | FRB |  | Incorrect Billing Option (REF*BLT) Requested |
|  | FRC |  | Incorrect Bill Calculation Type (REF*PC) Requested |
|  | MTI |  | Maintenance Type Code (ASI02) invalid |
|  | NCB |  | EGS not certified to provide requested bill option |
|  | Not valid in NJ |
|  | NEB |  | Customer not eligible for requested bill option |
|  | Not valid in NJ |
|  | SDE |  | Service Does Not Exist |
|  | PA Rules: Used ONLY when the LDC receives a request for a service that the state does not support. REF*1P*SNP is used if the LDC receives a request that the state supports, but the LDC does not. NJ Rules: In NJ it is valid to use the REF*1P*SNP at this time. |
|  | NIA |  | Not interval account |
|  | UND |  | Cannot identify ESP |
|  | UNE |  | Cannot identify LDC |
|  | W05 |  | Requested Rate not found or not in effect on the requested date (Rate Ready Only). |
| Optional | REF03 | 352 | Description | X | AN 1/80 |
|  | A free-form description to clarify the related data elements and their content |
|  | Used to further describe the Rejection Reason Codes sent in REF02. Codes “A13” and “API” require text explanation in this element. |

# Updated Detailed Specification, REF*17 (Additional REF02 Codes for Interval Detail Level)

# Segment:	REF Reference Identification (17=Summary Interval)

Position:	030

Loop:	LIN

Level:	Detail

Usage:	Optional

Max Use:	>1

Purpose:	To specify identifying information

Syntax Notes:	1	At least one of REF02 or REF03 is required.

2	If either C04003 or C04004 is present, then the other is required.

3	If either C04005 or C04006 is present, then the other is required.

Semantic Notes:	1	REF04 contains data relating to the value cited in REF02.

Comments:

| Notes: |  | When changing the indicator to receive both Interval Detail and Summary, or to only receive Summary level information, the LIN05 must have a value of “SI”. |
| --- | --- | --- |
| PA Use: |  | LDC to ESP Request: Response: ESP to LDC Request: Response: | Not Used Not Used Optional for PECO; Otherwise Not Used |
| NJ Use: |  | Same as PA (excluding PECO) –However, only supported by JCP&L and Atlantic City Electric |
| DE Use: |  | Not used in Delaware |
| MD Use: |  | Same as PA (excluding PECO) |
| Examples: |  | REF*17*SUMMARY REF*17*DETAIL REF*17*METERDETAIL (PECO Only) |

Data Element Summary

Ref.	Data

Des.	Element	Name	X12 Attributes

| Must Use | REF01 | 128 | Reference Identification Qualifier | M | ID 2/3 |
| --- | --- | --- | --- | --- | --- |
|  | Code qualifying the Reference Identification |
|  | 17 |  | Client Reporting Category |
|  | Used to convey whether the ESP will receive summary only information, or detail and associated summary information for this interval account. |
| Must Use | REF02 | 127 | Reference Identification | X | AN 1/30 |
|  | Reference information as defined for a particular Transaction Set or as specified by the Reference Identification Qualifier |
|  | When REF01 is 17, valid values for REF02 are: SUMMARY – Metering party will send only summary level data for this interval account. DETAIL – Metering party will send both summary and detail data for this interval account. PECO will interpret this as account-level detail. PECO-Only: METERDETAIL – Metering party will send interval details for each meter on the account |

# Updated Detailed Specification, Add REF*MT*REF03 (Interval Data Capability)

## Segment:	REF Reference Identification (MT=Meter Type)

Position:	130

Loop:	NM1

Level:	Detail

Usage:	Optional

Max Use:	>1

Purpose:	To specify identifying information

Syntax Notes:	1	At least one of REF02 or REF03 is required.

2	If either C04003 or C04004 is present, then the other is required.

3	If either C04005 or C04006 is present, then the other is required.

Semantic Notes:	1	REF04 contains data relating to the value cited in REF02.

Comments:

| PA Use: |  | There will be only be one REF*MT segment for each NM1 loop. If there are multiple meter types on this meter, only one REF*MT will be sent. It will contain the code COMBO. The specific meter type will be identified in the REF03 field in subsequent REF segments for this meter (i.e. REF*4P, REF*IX, REF*TU). |
| --- | --- | --- |
|  |  | LDC to ESP Request: Accept Response: Reject Response: ESP to LDC Request: Response: | Required for change of Meter Type, Meter Multiplier, # Dials and Type of usage sent on 867 Not Used Optional Not Used Not Used |
| NJ Use: |  | Same as PA |
| DE Use: |  | Same as PA |
| MD Use: |  | Same as PA |
| Example: |  | REF*MT*KHMON or REF*MT*COMBO |

Data Element Summary

Ref.	Data

Des.	Element	Name	X12 Attributes

| Must Use | REF01 | 128 | Reference Identification Qualifier | M | ID 2/3 |
| --- | --- | --- | --- | --- | --- |
|  | Code qualifying the Reference Identification |
|  | MT |  | Meter Ticket Number |
|  | Meter Type |
| Must Use | REF02 | 127 | Reference Identification | X | AN 1/30 |
|  | Reference information as defined for a particular Transaction Set or as specified by the Reference Identification Qualifier |
|  | When REF01 is MT, the meter type is expressed as a five-character field. The first two characters are the type of consumption, the last three characters are the metering interval. “COMBO” is used for a meter that records more than one measurement. Valid values can be a combination of the following values: |
|  | Type of Consumption |  | Metering Interval |
|  | K1 | Kilowatt Demand |  | Nnn | Number of minutes from 001 to 999 |
|  | K2 | Kilovolt Amperes Reactive Demand |  | ANN | Annual |
|  | K3 | Kilovolt Amperes Reactive Hour |  | BIA | Bi-annual |
|  | K4 | Kilovolt Amperes |  | BIM | Bi-monthly |
|  | K5 | Kilovolt Amperes Reactive |  | DAY | Daily |
|  | KH | Kilowatt Hour |  | MON | Monthly |
|  | T9 | Thousand Kilowatt Hours |  | QTR | Quarterly |
|  | For Example: |
|  |  | KHMON | Kilowatt Hours Per Month |  |  |
|  |  | K1015 | Kilowatt Demand per 15 minute interval |  |  |
|  | Other Valid Codes |  |  |
|  | COMBO | This code is used to indicate that the meter has multiple measurements, e.g., one meter that measures both kWh and Demand. |

| Optional | REF03 | 127 | Reference Identification Qualifier | X | AN 1/80 |
| --- | --- | --- | --- | --- | --- |
|  | Reference information as defined for a particular Transaction Set or as specified by the Reference Identification Qualifier |
|  | NOTE: PECO (PA) is the only EDC currently populating this segment. When REF01 is MT, valid values for REF03 are: I – Interval data available M –Interval data not available |

Scenario 6:  ESP change, from summary to detailed, specifying meter-level

EDI 814 Change Request from ESP

| BGN*13*1999040111956531*19990401 | Request, unique transaction identification number and transaction creation date |
| --- | --- |
| N1*8S*LDC COMPANY*1*007909411**40 | LDC Name, LDC DUNS information, receiver |
| N1*SJ*ESP COMPANY*9*007909422ESP1**41 | ESP Name, ESP DUNS information, submitter |
| N1*8R*CUSTOMER NAME | Customer Name |
| LIN*CHG1999123108000001*SH*EL*SH*SI | Unique transaction reference number, electric generation services |
| ASI*7*001 | Change Request |
| REF*TD*REF17 | Change Reason Indicating change in Interval Status |
| REF*11*3452344567 | ESP Account Number |
| REF*12*2931839200 | LDC Account Number |
| REF*17*METERDETAIL | Interval Status |

EDI 814 Change Response from EDC

| BGN*11*1999040212001*19990401***1999040111956531 | Response, unique transaction identification number and transaction creation date |
| --- | --- |
| N1*8S*LDC COMPANY*1*007909411**41 | LDC Name, LDC DUNS information, submitter |
| N1*SJ*ESP COMPANY*9*007909422ESP1**40 | ESP Name, ESP DUNS information, receiver |
| N1*8R*CUSTOMER NAME | Customer Name |
| LIN*CHG1999123108000001*SH*EL*SH*SI | Unique transaction reference number, electric generation services |
| ASI*WQ*001 | Accept Change Request |
| REF*11*3452344567 | ESP Account Number |
| REF*12*2931839200 | LDC Account Number |
| DTM*007*19990415 | Effective Date of Change |

Scenario 7:  ESP change, from detailed meter-level to summary

EDI 814 Change Request from ESP

| BGN*13*1999040111956531*19990401 | Request, unique transaction identification number and transaction creation date |
| --- | --- |
| N1*8S*LDC COMPANY*1*007909411**40 | LDC Name, LDC DUNS information, receiver |
| N1*SJ*ESP COMPANY*9*007909422ESP1**41 | ESP Name, ESP DUNS information, submitter |
| N1*8R*CUSTOMER NAME | Customer Name |
| LIN*CHG1999123108000001*SH*EL*SH*SI | Unique transaction reference number, electric generation services |
| ASI*7*001 | Change Request |
| REF*TD*REF17 | Change Reason Indicating change in Interval Status |
| REF*11*3452344567 | ESP Account Number |
| REF*12*2931839200 | LDC Account Number |
| REF*17*SUMMARY | Interval Status |

EDI 814 Change Response from EDC

| BGN*11*1999040212001*19990401***1999040111956531 | Response, unique transaction identification number and transaction creation date |
| --- | --- |
| N1*8S*LDC COMPANY*1*007909411**41 | LDC Name, LDC DUNS information, submitter |
| N1*SJ*ESP COMPANY*9*007909422ESP1**40 | ESP Name, ESP DUNS information, receiver |
| N1*8R*CUSTOMER NAME | Customer Name |
| LIN*CHG1999123108000001*SH*EL*SH*SI | Unique transaction reference number, electric generation services |
| ASI*WQ*001 | Accept Change Request |
| REF*11*3452344567 | ESP Account Number |
| REF*12*2931839200 | LDC Account Number |
| DTM*007*19990415 | Effective Date of Change |

Scenario 8:  For NON-INTERVAL account:  ESP change, from summary to detailed, specifying account-level

EDI 814 Change Request from ESP

| BGN*13*1999040111956531*19990401 | Request, unique transaction identification number and transaction creation date |
| --- | --- |
| N1*8S*LDC COMPANY*1*007909411**40 | LDC Name, LDC DUNS information, receiver |
| N1*SJ*ESP COMPANY*9*007909422ESP1**41 | ESP Name, ESP DUNS information, submitter |
| N1*8R*CUSTOMER NAME | Customer Name |
| LIN*CHG1999123108000001*SH*EL*SH*SI | Unique transaction reference number, electric generation services |
| ASI*7*001 | Change Request |
| REF*TD*REF17 | Change Reason Indicating change in Interval Status |
| REF*11*3452344567 | ESP Account Number |
| REF*12*2931839200 | LDC Account Number |
| REF*17*DETAIL | Interval Status |

EDI 814 Change Response from EDC

| BGN*11*1999040212001*19990401***1999040111956531 | Response, unique transaction identification number and transaction creation date |
| --- | --- |
| N1*8S*LDC COMPANY*1*007909411**41 | LDC Name, LDC DUNS information, submitter |
| N1*SJ*ESP COMPANY*9*007909422ESP1**40 | ESP Name, ESP DUNS information, receiver |
| N1*8R*CUSTOMER NAME | Customer Name |
| LIN*CHG1999123108000001*SH*EL*SH*SI | Unique transaction reference number, electric generation services |
| ASI*U*001 | Reject Change Request |
| REF*7G*NIA*NOT INTERVAL ACCOUNT | Reject Reason |
| REF*11*3452344567 | ESP Account Number |
| REF*12*2931839200 | LDC Account Number |

Scenario 9:  EDC meter exchange, with new meter providing interval data

EDI 814 Change Request from EDC (one-to-one meter exchange)

| BGN*13*1999040111956531*19990401 | Request, unique transaction identification number and transaction creation date |
| --- | --- |
| N1*8S*LDC COMPANY*1*007909411**41 | LDC Name, LDC DUNS information, submitter |
| N1*SJ*ESP COMPANY*9*007909422ESP1**40 | ESP Name, ESP DUNS information, receiver |
| N1*8R*CUSTOMER NAME | Customer Name |
| LIN*CHG1999123108000001*SH*EL*SH*CE | Unique transaction reference number, electric generation services |
| ASI*7*001 | Request Change |
| REF*11*2348400586 | ESP Account Number |
| REF*12*2931839200 | LDC Account Number |
| DTM*007*19990415 | Effective Date of Change |
| NM1*MX*3******32*334545R | Start of Meter Exchange Loop, Meter Number being added |
| REF*46*345573R | Old Meter Number – indicates that this was a meter exchange |
| REF*TD*NM1MX | Change Reason indicating Meter Exchange |
| REF*LO*GS | Load Profile of New Meter |
| REF*NH*GS1 | LDC Rate Class of New Meter |
| REF*PR*123 | LDC Rate Subclass of New Meter |
| REF*RB*0300 | ESP Rate Code of New Meter |
| REF*TZ*18 | Meter Cycle of New Meter |
| REF*MT*COMBO*I | Meter Type of New Meter |
| REF*4P*1*KHMON | Meter Constant of New Meter |
| REF*IX*5.0*KHMON | Number of Dials on New Meter |
| REF*TU*51*KHMON | Consumption provided on the 867 |
| REF*4P*1*K1MON | Meter Constant of New Meter |
| REF*IX*5.0*K1MON | Number of Dials on New Meter |
| REF*TU*41*K1MON | Consumption provided on the 867 |
| REF*TU*42*K1MON | Consumption provided on the 867 |
| REF*TU*51*K1MON | Consumption provided on the 867 |

Data Dictionary changes

Updated REF*MT (meter type) with addition of REF03 for interval data capability:

| 79 | Meter Type | Type of Meter | REF02 & REF03 | NM1: REF01= MT | X(5) |
| --- | --- | --- | --- | --- | --- |

No changes to General or Pennsylvania Notes.

# Updated Detailed Specification, REF*17 (Additional REF02 Codes for Interval Detail Level)

# Segment:	REF Reference Identification (17=Summary Interval)

Position:	030

Loop:	LIN

Level:	Detail

Usage:	Optional

Max Use:	>1

Purpose:	To specify identifying information

Syntax Notes:	1	At least one of REF02 or REF03 is required.

2	If either C04003 or C04004 is present, then the other is required.

3	If either C04005 or C04006 is present, then the other is required.

Semantic Notes:	1	REF04 contains data relating to the value cited in REF02.

Comments:

| PA Use: |  | If the LDC supports the summary interval at the account level, the LDC will send the REF*17 segment as part of the reinstatement request. The value of the REF02 field for the REF*17 segment will either be “SUMMARY” or “DETAIL”. Note: The REF*17 is being sent under the LIN05 code of “CE” as part of the reinstatement. For PECO only: The REF*17 segment will either be “SUMMARY”, “DETAIL” (for account-level detail), or “METERDETAIL”. If the LDC only supports the summary interval data at the supplier level, no REF*17 segment will be sent as part of the reinstatement. |
| --- | --- | --- |
|  |  | Request: Response: | Conditional – always sent if the LDC supports setting of interval summary/detail at the account level, and this is an interval account. Will not be sent if the LDC supports setting of interval summary/detail at the supplier level. Not Used |
| NJ Use: |  | Optional. JCP&L will send “SUMMARY” value when Interval Summary has been established for this account. Not provided by the other EDCs. |
| DE Use: |  | Not Used |
| MD Use: |  | Same as PA (excluding PECO) |
| Example: |  | REF*17*SUMMARY |

Data Element Summary

Ref.	Data

Des.	Element	Name	X12 Attributes

| Must Use | REF01 | 128 | Reference Identification Qualifier | M | ID 2/3 |
| --- | --- | --- | --- | --- | --- |
|  | Code qualifying the Reference Identification |
|  | 17 |  | Client Reporting Category |
|  | Used to convey whether the supplier will receive summary only information for this interval account, or whether the supplier will receive detail and associated summary information for this interval account. |
| Must Use | REF02 | 127 | Reference Identification | X | AN 1/30 |
|  | Reference information as defined for a particular Transaction Set or as specified by the Reference Identification Qualifier |
|  | When REF01 is 17, valid values for REF02 are: SUMMARY – Metering party will send only summary level data for this interval account. DETAIL – Metering party will send detail data and its associated summary information for this interval account. PECO will interpret this as account-level detail. PECO-Only: METERDETAIL – Metering party will send interval details for each meter on the account |

# Updated Detailed Specification, Add REF*MT*REF03 (Interval Data Capability)

## Segment:	REF Reference Identification (MT=Meter Type)

Position:	130

Loop:	NM1

Level:	Detail

Usage:	Optional

Max Use:	>1

Purpose:	To specify identifying information

Syntax Notes:	1	At least one of REF02 or REF03 is required.

2	If either C04003 or C04004 is present, then the other is required.

3	If either C04005 or C04006 is present, then the other is required.

Semantic Notes:	1	REF04 contains data relating to the value cited in REF02.

Comments:

| PA Use: |  | There will be only be one REF*MT segment for each NM1 loop. If there are multiple meter types on this meter, only one REF*MT will be sent. It will contain the code COMBO. The specific meter type will be identified in the REF03 field in subsequent REF segments for this meter (i.e. REF*4P, REF*IX, REF*TU). |
| --- | --- | --- |
|  |  | Request: Response: | Required for each meter that is used for billing purposes. This segment will not be provided in the NM1 loop for UNMETERED services. Not Used |
| NJ Use: |  | Same as PA |
| DE Use: |  | Same as PA |
| MD Use: |  | Same as PA |
| Example: |  | REF*MT*KHMON or REF*MT*COMBO |

Data Element Summary

Ref.	Data

Des.	Element	Name	X12 Attributes

| Must Use | REF01 | 128 | Reference Identification Qualifier | M | ID 2/3 |
| --- | --- | --- | --- | --- | --- |
|  | Code qualifying the Reference Identification |
|  | MT |  | Meter Ticket Number |
|  | Meter Type |
| Must Use | REF02 | 127 | Reference Identification | X | AN 1/30 |
|  | Reference information as defined for a particular Transaction Set or as specified by the Reference Identification Qualifier |
|  | When REF01 is MT, the meter type is expressed as a five-character field. The first two characters are the type of consumption, the last three characters are the metering interval., except for the combination meter that records more than one measurement and is noted as "COMBO". Valid values can be a combination of the following values: |
|  | Type of Consumption |  | Metering Interval |
|  | K1 | Kilowatt Demand |  | Nnn | Number of minutes from 001 to 999 |
|  | K2 | Kilovolt Amperes Reactive Demand |  | ANN | Annual |
|  | K3 | Kilovolt Amperes Reactive Hour |  | BIA | Bi-annual |
|  | K4 | Kilovolt Amperes |  | BIM | Bi-monthly |
|  | K5 | Kilovolt Amperes Reactive |  | DAY | Daily |
|  | KH | Kilowatt Hour |  | MON | Monthly |
|  | T9 | Thousand Kilowatt Hours |  | QTR | Quarterly |
|  | For Example: |
|  |  | KHMON | Kilowatt Hours Per Month |  |  |
|  |  | K1015 | Kilowatt Demand per 15 minute interval |  |  |
|  | Other Valid Codes |  |  |
|  | COMBO | This code is used to indicate that the meter has multiple measurements, e.g., one meter that measures both kWh and Demand. |
| Optional | REF03 | 127 | Reference Identification Qualifier | X | AN 1/80 |
|  | Reference information as defined for a particular Transaction Set or as specified by the Reference Identification Qualifier |
|  | NOTE: PECO (PA) is the only EDC currently using this segment. When REF01 is MT, valid values for REF03 are: I – Interval data available M – Monthly; Interval data not available |

Scenario 10:  EDC Reinstatement, detailed account-level data

Bill Ready Reinstatement – From EDC

(modified from January 2012 EDI 814 IG, shown with modified REF*MT and new REF*IDL segments;  Also added REF*17 since example does not include it)

| BGN*13*199904011956531*19990401 | BGN segment indicating this is a Request transaction. |
| --- | --- |
| N1*8S*LDC COMPANY*1*007909411**41 | LDC Name, LDC DUNS information, submitter |
| N1*SJ*ESP COMPANY*9*007909422ESP1**40 | ESP Name, ESP DUNS information, receiver |
| N1*8R*CUSTOMER NAME*92*1210 | Customer Name and reference number |
| N3*123 N MAIN ST*FLR 13 | Service address |
| N4*ANYTOWN*PA*18111 | City/State/Zip for Service Address. |
| PER*IC*MARY JONES*TE*8005559876 | Customer Contact name and telephone number |
| N1*BT*ACCOUNTS PAYABLE DEPT | Bill to party |
| N3*100 WEST AVENUE | Bill to address |
| N4*ANYTOWN*PA*18111 | Bill to City/State/Zip |
| PER*IC*KELLY WEST*TE*8005559876 | Bill To Contact name and telephone number |
| N1*PK*FRANK SMITH | Party to Receive Copy Name |
| N3*459 AVENUE B | Party to Receive Copy Address |
| N4*ANYTOWN*PA*18111 | Party to Receive Copy City/State/Zip |
| PER*IC*FRANK SMITH*TE*8005559876 | Party to Receive Copy Name |
| N1*2C*CAROL WRIGHT | Co-Participant Name |
| N3*23948 MAIN STREET | Co-Participant Address |
| N4*ANYTOWN*PA*18111 | Co-Participant City/State/Zip |
| PER*IC*CAROL WRIGHT*TE*8005559876 | Co-Participant Name and telephone number |
| LIN*REIN19991231002*SH*EL*SH*CE | Transaction reference number, and enrollment request for generation services |
| ASI*7*025 | Reinstatement Request |
| REF*11*2348400586 | ESP Account Number |
| REF*12*293839200 | LDC Account Number |
| REF*BF*18 | LDC Billing Cycle |
| REF*BLT*LDC | LDC consolidates the LDC and ESP charges |
| REF*PC*DUAL | Each party calculates its own charges (Bill Ready) |
| REF*NR*N | Budget Billing Status |
| REF*17*DETAIL | Interval Status |
| REF*SPL**PJM192478939901287748 | Indicates PJM LMP Bus Number |
| DTM*007*19990401*1430*ET | Customer contacted LDC to reinstate ESP. |
| DTM*150*19990425 | Estimated Start Date |
| AMT*7N*1 | Participating interest |
| AMT*5J*2 | Air conditioners in load cycling program |
| AMT*L0*1 | Water Heaters in load cycling program |
| AMT*QY*1 | Eligible Load Percentage |
| AMT*KC*12.8 | Peak Load Capacity |
| AMT*KZ*14.1 | Network Service Peak Load |
| NM1*MQ*3******32*123857G | Meter Number |
| REF*LO*GS | LDC Load Profile |
| REF*NH*GS1 | LDC Rate class |
| REF*PR*123 | LDC Rate Subclass |
| REF*TZ*18 | LDC Meter Reading Cycle |
| REF*MT*COMBO*I | Meter Type |
| REF*4P*1*KHMON | Meter constant on the kWh register |
| REF*IX*6.1*KHMON | Number of dials/digits |
| REF*TU*41*KHMON | Off peak metering information sent on the 867 |
| REF*TU*42*KHMON | On peak metering information sent on the 867 |
| REF*4P*1*K1MON | Meter constant on the demand (kW) register |
| REF*IX*5.0*K1MON | Number of dials/digits |
| REF*TU*41*K1MON | Off Peak metering information sent on the 867 |
| REF*TU*42*K1MON | On Peak metering information sent on the 867 |
| NM1*MQ*3******32*218737S | Meter Number |
| REF*LO*GS | LDC Load Profile |
| REF*NH*GS1 | LDC Rate class |
| REF*PR*123 | LDC Rate Subclass |
| REF*TZ*18 | LDC Meter Cycle |
| REF*MT*KHMON | Meter Type |
| REF*4P*1*KHMON | Meter Constant |
| REF*IX*5.0*KHMON | Number of dials/digits |
| REF*TU*51*KHMON | Totalized metering information sent on the 867 |

Reinstatement responses from the ESP remain unchanged.